## Slide 1
Master of Science HES-SO in Engineering
Orientation : Technologies industrielles (TIN)
Low-complexity scalable IoT framework
Fait par Lucas Bonvin
Sous la direction de
Prof. Dominique Gabioud
Dans l’institut de recherche énergie et environnement de la HES-SO Valais-Wallis
[Expert externe Alain Woeffray, Co-fondateur Des Choses Pareilles]

## Slide 2: Low-complexity scalable IoT framework Summary
Introduction
Analysis
Conception
Tests and Results
Conclusion
Notes: Low scalable … vous dit pas grand-chose -> introduction sur l’IoT

## Slide 3: Introduction: The IoT world and cloud.iO 1/2
  Where does all this data go?
The Internet of Things
41.6 billions of connected devices by 2025[1]
20.6 Zettabytes of data exchange by 2021[2]
Notes: 1 international data corporation
2 cisco

## Slide 4: Introduction: The IoT world and cloud.iO 2/2
Cloud-based frameworks
More than 152 clouds (postcapes.com) + cloud.iO
cloud.iO was created at the HES-SO Valais-Wallis for research projects [3]
Endpoint
Endpoint
Notes: User possède des Endpoints

## Slide 5: Analysis : Specifications
Analysis of the IoT landscape, positioning new cloud.iO v0.2
Collection of requirements for cloud.iO v0.2, elaboration of the specification
Development, documentation, test and validation of cloud.iO v0.2
From cloud.iO v0.1 to cloud.iO v0.2

## Slide 6: Analysis: State of the art
What features define an IoT cloud framework?
Thing Monitoring (Digital Twin)
Thing History
History Visualisation
Remote Job Execution
Rules Engine
Cloud Computing

## Slide 7: Analysis: State of the art
On-premise deployment
Specific Hardware
SDK/API
Edge Computing
Interoperability
What features define an IoT cloud framework?

## Slide 8: Analysis: cloud.iO v0.1 1/2
  Spring.io
    Micro-service Platform
    Open source
  RabbitMQ
    Message Broker
    Support AMQP and MQTT
    Open source
  MQTT
    Messaging protocol
    Support TLS/SSL
    Authentication using x509 certificate
  MongoDB and InfluxDB
    Database
    Free Software
  Two libraries (SDK)
    Java
    Python

## Slide 9: Analysis: cloud.iO v0.1 2/2
Low-complexity: multiple simple services
Scalability: services distributed on multiple computing node
Extensibility: new services easily added
Low-complexity scalable IoT framework

## Slide 10: Analysis: cloud.iO v0.1: Architecture
Notes: Utilisateur possède des endpoints

## Slide 11: Analysis: cloud.iO v0.1: Messaging Protocol
Exchanges
Queues
X
Message Broker
route
X
X
X
Producer
Consumer
publish
 | MQTT | AMQP
Simple Topic | example.toto.titi | example/toto/titi
Single Level Wildcard | example.+.titi | example/*/titi
Multi-Level Wildcard | example.# | example.#

## Slide 12
Attribute Type:
Bool
Integer
Number
String
Attribute Constraint:
Static: Read-only, Static value
Status: Read-only, computed value
Measure: Read-only, represent physical process
Parameter: Read/Write, change the Endpoint’s behavior, persistent
SetPoint: Read/Write, Control value, non-persistent
Analysis: cloud.iO v0.1: From Endpoint to Attribute

## Slide 13
Analysis: cloud.iO v0.1: From Endpoint to Attribute
Attribute Type:
Bool
Integer
Number
String
Attribute Constraint:
Static: Read-only, Static value
Status: Read-only, computed value
Measure: Read-only, represent physical process
Parameter: Read/Write, change the Endpoint’s behavior, persistent
SetPoint: Read/Write, Control value, non-persistent

## Slide 14
@update/…/AttributeName
@set/…/AttributeName
@online/EndpointUUID
@offline/EndpointUUID
@nodeAdded/…/ NodeNameToAdd
@nodeRemoved/…/NodeNameToRemove
Topic: @update/EndpointUUID//node/myHeater/object/temperatures/attribute/temperature
@prefix/EndpointUUID/node/nodeName/object/objectName/.../attribute/attributeName
Analysis: cloud.iO v0.1: From Endpoint to Attribute
{
"type": "Number",
"constraint": "Measure",
"timestamp":1575547591859.0,
"value": 25
}
Notes: Mot clef qui definisse la structure

## Slide 15: Analysis: Enhance cloud.iO, feedback from users
Redefine topic & access control
Logging
Update of Endpoint/Node/Object
Certificate creation
log

## Slide 16: Analysis: Enhance cloud.iO, IoT framework analysis
Notes: Seul chose à relever: interoperabilité

## Slide 17: Analysis: Enhance cloud.iO, IoT framework analysis
Notes: On y reviens durant la synthèse de l’analyse

## Slide 18: Analysis: Interoperability

## Slide 19: Analysis: Interoperability Web of Thing
  World Wide Web Consortium (W3C)
    Standardization organism
    Behind HTLM, RDF, CSS, PNG, SVG, ...
    Standardization of the IoT
  Web Of Thing (WoT)
    Candidate Recommendation [4][5]
    Enhance IoT Interoperability
    Define a data model for the Things :TD
    TD contain a self-describing API

## Slide 20: Analysis: Interoperability TD
{
"@context": "https://www.w3.org/2019/wot/td/v1",
"id": "urn:heater",
"title": "myHeater",
"securityDefinitions": {
"basic_sc": {
"scheme": "basic",
"in": "header"
}
},
"security": ["basic_sc"],
"properties": {
"temperature": {
"type": "integer",
"forms": [{"href": "https://myHeater.com/get"}]
},
"setPointTemperature": {
"type": "integer",
"forms": [{"href": "https://myHeater.com/set"}]
}
},
"actions": {
"toggleRegulation": {
"forms": [{"href": "https://myHeater.com/toggle"}]
}
},
"events": {
"temperatureChange": {
"data": {
"type": "integer"
},
"forms": [{"href": "https://myHeater.com/change"}]
}
}
}

## Slide 21: Analysis: Interoperability TD
{
"@context": "https://www.w3.org/2019/wot/td/v1",
"id": "urn:heater",
"title": "myHeater",
"securityDefinitions": {
"basic_sc": {
"scheme": "basic",
"in": "header"
}
},
"security": ["basic_sc"],
"properties": {
"temperature": {
"type": "integer",
"forms": [{"href": "https://myHeater.com/get"}]
},
"setPointTemperature": {
"type": "integer",
"forms": [{"href": "https://myHeater.com/set"}]
}
},
"actions": {
"toggleRegulation": {
"forms": [{"href": "https://myHeater.com/toggle"}]
}
},
"events": {
"temperatureChange": {
"data": {
"type": "integer"
},
"forms": [{"href": "https://myHeater.com/change"}]
}
}
}
: Meta data

## Slide 22: Analysis: Interoperability TD
"properties": {
"temperature": {
"type": "integer",
"forms": [{"href": "https://myHeater.com/get"}]
},
"setPointTemperature": {
"type": "integer",
"forms": [{"href": "https://myHeater.com/set"}]
}
},
"actions": {
"toggleRegulation": {
"forms": [{"href": "https://myHeater.com/toggle"}]
}
},
"events": {
"temperatureChange": {
"data": {
"type": "integer"
},
"forms": [{"href": "https://myHeater.com/change"}]
}
}
}
: Interaction Affordances

## Slide 23: Analysis: Synthesis
From users’ feedback
From cloud analysis
Redefine topic & access control
Logging
Update of Endpoint/Node/ Object
Certificate creation
Remote Job Execution
API (RESTful)
Interoperability
log

## Slide 24: Conception: Topic & Access Control 1/2
cloud.iO v0.1
Permission only on Endpoints
cloud.iO v0.2
Access control based on topic
Introduction of prioritized permission
Introduction of user group
@prefix/EndpointUUID/
nodeName/
node/
object/
objectName/
…/
attribute/
attributeName
Notes: Structure est fix 1 endpoint, 1 node, 1 ou plus object, 1 attribute

## Slide 25: Conception: Topic & Access Control 1/2
cloud.iO v0.1
Permission only on Endpoints
cloud.iO v0.2
Access control based on topic
Introduction of prioritized permission
Introduction of user group
@prefix/EndpointUUID/
nodeName/
objectName/
…/
attributeName

## Slide 26: Conception: Topic & Access Control 2/2
{
" permissions ": {
" endpointUUID /#": {
"permission": "WRITE",
"priority": "LOW"
},
"endpointUUID/mySecondHeater/#": {
"permission": "DENY",
"priority": "HIGH"
},
"endpointUUID/myHeater/temperatures
↳/setPointTemperature ": {
"permission": "READ",
"priority": "HIGHEST"
}
}
}

## Slide 27: Conception: Remote Job Execution
  Remote Jobs Execution
    Execute Shell script remotely
    Possibility to retrieve output of script
  Pre-implemented command
    Listing all available commands/scripts
    Update Scripts from an URL
Topic: @exec/ bc0f1bf8-bdae-11e9-9cb5-2a2ae2dbcce4
{
"jobURI": "cmd://listJobs",
"correlationID": "1a45a6ca",
"data": "",
"sendOutput": true
}
{
"data": "This is a Job output",
"correlationID": "1a45a6ca"
}
Topic: @execOutput/ bc0f1bf8-bdae-11e9-9cb5-2a2ae2dbcce4

## Slide 28: Conception: Remote Job Execution

## Slide 29: Conception: Logging
Topic: @logs/ bc0f1bf8-bdae-11e9-9cb5-2a2ae2dbcce4
Topic: @logsLevel/ bc0f1bf8-bdae-11e9-9cb5-2a2ae2dbcce4
{
"level": "TRACE"
}
{
"level": "ERROR",
"timestamp": 1577802897012,
"message": "Data Error",
"loggerName": "HeaterLogger",
"logSource": "Heater/main, line 27"
}
  Logging
    Saved as time-series
    Possibility to filter by log level
    Retrieve through RESTful API
    User Log4j
  Different log level
    OFF
    FATAL
    ERROR
    WARN
    INFO
    DEBUG
    TRACE
    ALL

## Slide 30: Conception: Transaction
Problematic:
cloud.iO v0.1 Can only update one attribute at a time
Solution:
Transaction
  beginTransaction()
  commitTransaction()
  rollbackTransaction()
Topic: @transaction/ bc0f1bf8-bdae-11e9-9cb5-2a2ae2dbcce4
{
"attributes": {
"endpointUUID/…/exampleAttribute1": {
"constraint": "Measure",
"timestamp": 1577802897520,
"type": "Number",
"value": 25.1
},
"endpointUUID/…/exampleAttribute2": {
"constraint": "Measure",
"timestamp": 1577802897750,
"type": "Number",
"value": 23.1
},
"endpointUUID/…/exampleAttribute3": {
"constraint": "Status",
"timestamp": 1577802898290,
"type": "String",
"value": "Example"
}
}
}

## Slide 31: Conception: Certificate Management
In cloud.iO v0.1: Manually by an administrator
In cloud.iO V0.2: Generated by the cloud, available through RESTful API
  Generating certificate and private key
  Generating certificate from public key
  Generating Zip files with certificates and config file for SDK

## Slide 32: Conception: RESTful API
  Http tools
    User authentication
    Support Https
  Tools for User and Administrator
    User & User Group Management
    Endpoint Management
    Certificate
    History
    Logging
    Remote Jobs Execution
…

## Slide 33: Conception: RESTful API, multiple challenges
Problematics | Solutions
Authentication | Use of access control database, custom User Details Service
Retrieving certificates | Sending files, custom Response Entity
Getting notified of attribute change | Longpoll
Re-create the Remote Jobs execution messages sequence | Server-sent events

## Slide 34: Conception: Web Of Things Compliance 1/2
Thing
WoT Servient
Expose
Application
WoT Servient
Interact
Consume
TD Consumer

## Slide 35: Conception: Web Of Things Compliance 2/2
{
"@context": "https://www.w3.org/2019/wot/td/v1",
"id": "urn:bc0f1bf8-bdae-11e9-9cb5-2a2ae2dbcce4:myHeater",
"title": "myHeater",
"securityDefinitions": {
"https_sc": {
"scheme": "basic",
"in": "query"
},
"mqtts_sc": {"scheme": "cert"}
},
"security": [
"https_sc",
"mqtts_sc"
],
"properties": {
"endpointUUID.myHeater.temperatures.setPointTemperature": {
  ...
},
"events": {
"endpointUUID.myHeater.temperatures.setPointTemperature": {
...
}
}

## Slide 36: Conception: Web Of Things Compliance 2/2
"type": "object",
"properties": {
"constraint": {"type": "string", "enum": ["SetPoint"]},
"type": {"type": "string", "enum": ["Integer"]},
"timestamp": {"type": "number"},
"value": {"type": "number"}
},
"required": ["constraint","type","timestamp","value"],
"forms": [
{
"href": "https://cloud.iO:8081/api/v1/getAttribute/endpointUUID.…",
"op": "readproperty",
"contentType": "application/json"
},
{
"href": "mqtts://cloud.iO:8883/@set/endpointUUID/…",
"op": "writeproperty",
"contentType": "application/json“
},
{
"href": "https://cloud.iO:8081/api/v1/setAttribute/endpointUUID.…",
"op": "writeproperty",
"contentType": "application/json"
}
"properties": {
"endpointUUID.myHeater.temperatures.setPointTemperature": {
},
"events": {
"endpointUUID.myHeater.temperatures.setPointTemperature": {
...
}
}
Notes: Même type de structure pour event

## Slide 37: Conception: cloud.iO v0.2 architecture, messaging

## Slide 38: Conception: cloud.iO v0.2 architecture, RESTful API

## Slide 39: Tests and Results: Web of Thing TD Evaluation
JSON validation
WoT recommendation validation
JSON validation with with JSON Schema
JSON-LD validation

## Slide 40: Tests and Results: Performances Evaluation 1/2
Database linked service
Use of Batch for InfluxDB

## Slide 41: Tests and Results: Performances Evaluation 2/2
Use case: send mqtt message, retrieve it with mqtt and http

## Slide 42: Tests and Results: Evaluation the API and demonstrator
Evaluation of API
Test during implementation with http client (Insomnia)
55 unit tests with 140 use cases
Demonstrator

## Slide 43: Conclusion: Project Overview
Specification for cloud.iO established
Implemented and tested functionality
Lack of tests with a deployed version of cloud.iO v0.2
Redefine topic & access control
Logging
Transaction
Certificate creation
Remote Job Execution
API (RESTful)
Interoperability
log
Notes: On a fait un papier!

## Slide 44: Conclusion: Future Improvement
Authentication using JSON Web Token (JWT) [6]
Continuous work on W3C WoT
Other web technologies (WebSocket, MQTT over WebSocket, …)
More languages support for Endpoint Library

## Slide 45: Questions?

## Slide 46: References
[1] IDC, “The Growth in Connected IoT Devices Is Expected to Generate 79.4ZB of Data in 2025, According to a New IDC Forecast,” 2019, https://www.idc.com/getdoc.jsp?containerId=prUS45213219.
[2] Cisco and/or its affiliates, “Cisco Global Cloud Index: Forecast and Methodology, 2016–2021,” 2018.
[3] P. Roduit, D. Gabioud, G. Basso, G. Maitre, and P. Ferrez, “cloud.io: A decentralised iot architecture to control electrical appliances in households,” in Smart Cities, Green Technologies and Intelligent Transport Systems,
B. Donnellan, C. Klein, M. Helfert, and O. Gusikhin, Eds. Cham: Springer International Publishing, 2019, pp. 67–89.
[4] M. Kovatsch, R. Matsukura, M. Lagally, T. Kawaguchi, K. Toumura, and K. Kajimoto, “Web of Things (WoT) Architecture,” 2019, https://www.w3.org/TR/wot-architecture/.
[5] S. Kaebisch, T. Kamiya, M. McCool, V. Charpenay, and M. Kovatsch, “Web of Things (WoT) Thing Description,” 2019, https://www.w3.org/TR/wot-thing-description/.
[6] JSON Web Token (JWT), Internet Engineering Task Force, 05 2015. [Online]. Available: https://tools.ietf.org/html/rfc7519